## Slide 1: TRANSESOPHAGEAL ECHOCARDIOGRAPHY BASIC VIEWS, CONTRAINDICATIONS AND COMPLICATIONS
KATHIRVEL SUBRAMANIAM MD MPH
ASSOCIATE PROFESSOR OF ANESTHESIOLOGY
UNIVERSITY OF PITTSBURGH
PITTSBURGH PA, USA

## Slide 2: Goals
Review the equipment
Review the safety considerations
Standard Basic TEE Examination views

## Slide 3: SAFETY
Know your patient
Know your equipment

## Slide 4: TEE PROBE
PROBE TIP
PROBE SHAFT
PROBE HANDLE
PLUG IN SOCKET

## Slide 5: Probe manipulations
SMALL WHEEL
(LATERAL FLEXION)
BIG WHEEL (ANTE/RETROFLEX)
CRYSTAL MANIPULATION
LOCK

## Slide 6: Probe manipulations

## Slide 7: TEE IS SEMIINVASIVE!
Informed consent from the patient or next of kin
Consent need not be obtained during life threatening emergencies
NG tube can be left in place
Aspirate gastric contents
Check the position of NGT after removal of TEE probe
Review the indication for TEE
Look for contraindications for the procedure

## Slide 8: Contraindications
Absolute
Active GI Bleeding
Recent history of GI bleeding
Recent esophageal or gastric surgery
Esophageal obstruction from tumor or stricture
Poor airway control
Zenker Diverticulum, Pharyngeal pouch
Severe Cervical spine disease or injury
Esophageal trauma, Facial trauma
Relative
Barret Esophagus
Hiatal Hernia
Esophageal varices, web
Radiation therapy
Previous bariatric surgery
Thoracic aortic aneurysm
Dysphagia
Coagulopathy

## Slide 9: STANDARD TEE EXAMINATION
Basic TEE views only will be discussed
11 Views as recommended by American Society of Echocardiography/Society of Cardiovascular Anesthesiologists
Mid-esophageal, Trans-gastric and Aortic views

## Slide 10: Upper Esophageal (25 cm) / Mid-Esophageal (35 CM)

## Slide 11: Trans-gastric (40 cm) / Deep Trans-gastric (50 cm)

## Slide 12: Standard basic TEE examination

## Slide 13: Mid-esophageal 4 Chamber view
Depth 30-35cm
Center MV and LV in sector display
  clockwise or counterclockwise probe rotation
Adjust depth so LV apex is visible (Foreshortening of apex common with TEE)
Multiplane angle rotation to 10-20o

## Slide 14: ME 4-chamber view Structures
RA
IAS
LA
AMVL
PMVL
TVSL
TVPL
RV
LV
IVS

## Slide 15: ME 4 Chamber view
AL WALL
INFERO
SEPTAL
APEX

## Slide 16: ME 4 Chamber view Clinical utility
Global RV, LV function
Tricuspid Annular plane motion (RV Function)
Regional LV: Inferoseptal and Anterolateral walls
Color flow doppler over MV, TV, IAS to evaluate for pathology and shunt (Nyquist Limit 50-60 cm / sec)
Bowing of IAS, IVS indicates pressure differences

## Slide 17: ME Two Chamber View
Rotate multiplane angle to 80 - 100o until RV disappears
Global/Regional LV function: Anterior and Inferior Walls
MV structure and function (add CFD)
Left atrial appendage evaluation for clots

## Slide 18: ME 2 Chamber view
ANTERIOR WALL
INFERIOR WALL

## Slide 19: Left Atrial Appendage evaluation (ME 2C view)

## Slide 20: ME LONG AXIS VIEW
From ME 2Ch View rotate multiplane angle to 120-160o
  LVOT and AV will appear
Anteroseptal and Inferolateral LV walls
Apply CFD to MV, LVOT, AV for valvular disease

## Slide 21: ME Long Axis View
RV
ANTERO
SEPTAL
INFERO
LATERAL

## Slide 22: AV Long axis measurements

## Slide 23: ME Ascending aortic Long Axis view
From ME LAX view withdraw probe until the long axis view of ascending aorta comes in to view
Right PA will be seen in SAX posterior to ascending aorta

## Slide 24: ME Ascending aortic long axis view
RT PA
ASCENDING AORTA

## Slide 25: ME Ascending aortic Short Axis View
From ME Asc LAX view, rotating multiplane to 20-40o will reveal the proximal Ascending Aorta and SVC in SAX, bifurcation of PA
Proximal pulmonary emboli in main PA, Saddle, or R PA are sometimes found in this view

## Slide 26: ME Ascending aortic Short Axis

## Slide 27: ME Aortic valve short axis
From the ME Asc Aortic SAX view advancing the probe and the multiplane angle to 45-60o will reveal the AV in short axis
All three cusps of the AV can be clearly identified in this view

## Slide 28: ME Aortic Valve Short Axis

## Slide 29: ME RV Inflow-Outflow View
From ME Asc Aortic Valve SAX view, advance and turn probe clockwise while rotating multiplane angle to 60-90o until RVOT and PV seen
Estimate PAPs from TR jet peak velocity in this view
  PAPs = 4v2 + RAP

## Slide 30: ME RV Inflow-Outflow View

## Slide 31: ME Bicaval View
From RV inflow-outflow view rotate multiplane angle to 90-110o to obtain view of SVC and IVC
Catheters, pacing wires in svc and / or entering RA seen here
Evaluation of intra-atrial shunt (PFO, ASD), by CFD and / or ‘bubble’ study
Evaluation of Pulmonary artery systolic pressure

## Slide 32: ME Bicaval View

## Slide 34: Transgastric Mid-papillary Short Axis
From ME 4Ch view (multiplane angle at zero) advance probe to stomach, anteflex to make contact with gastric wall and view LV in SAX
Extremely important to visualize and identify the papillary muscles; posterior-medial and anterior-lateral papillary muscles
Only view that myocardium supplied by all 3 main coronary arteries are seen
Estimate LVEF, volume status, pericardial effusions, RWMA’s

## Slide 37: Descending aorta
The descending aorta is easily seen to the left of the heart and therefore from the ME 4Ch view (at 0 degrees) turn the probe to the left (counterclockwise) until the descending thoracic aorta is seen.
With the SAX of the descending thoracic aorta in view, change the multiplane angle to 90o shows the LAX view

## Slide 38: Descending aorta

## Slide 39: Complications

## Slide 41: Major injuries
Perforation 1-4 in 10,000 TEE examinations
Mortality 10-56%
Length of time between the perforation and diagnosis determines prognosis

## Slide 43: Upper GI injury

## Slide 44: Gastric injuries

## Slide 45: Operator factors
Probe not neutral during insertions and advancement
Insertion against resistance
Extreme frequent manipulations (extreme anteflexion) to get good images
Multiple operators rather than a single experienced examination
Limited examination ( ME views only in patients with gastric or GE junction pathology)

## Slide 46: Chemical injury
Venticinque, Steven G. MD*; Kashyap, Vikram S. MD†; O’Connell, Robert J. MD‡. Chemical Burn Injury Secondary to Intraoperative Transesophageal Echocardiography. Anesth Analg 2003;97:1260-1261

## Slide 47: BIOSAFETY
INTENSITY OF EXPOSURE (POWER, AMPLITUDE, FREQUENCY)
EXPOSURE TIME
TISSUE PERFUSION
TISSUE DENSITY

## Slide 48: Thermal injury
Ultrasound piezo-electric vibrations
Ultrasound energy absorption by tissues- heating of tissues
Doppler and color flow imaging
No strong evidence
Freeze or disconnect probe while not use
Automatic probe off when temperature reached 42-46

## Slide 49: Cavitation
Creation or vibration of small gas filled bodies by the ultrasound beam
Expansion and rarefaction of bubbles can cause cell damage
2D IMAGING

## Slide 50: Other complications
Endotracheal tube extubation/misplacement
Respiratory (Laryngospasm, Bronchospasm, Aspiration, Desaturation requiring intubation)
Circulatory (Hypertensive response, Cardiac arrhythmias, Aneurysm rupture)

## Slide 51: INDICATIONS FOR PERIOPERATIVE TEE Cardiac surgery
All Cardiac and thoracic aortic procedures
Catheter based intracardiac procedures

## Slide 52: Critical Care
TEE should be used when diagnostic information that is expected to alter management cannot be obtained by TTE or other modalities in a timely manner

## Slide 53: Non-cardiac surgery
TEE should be used when unexplained life threatening circulatory instability persists despite corrective therapy (Treatment)
TEE may be used when the nature of the planned surgery or the patient’s known or suspected cardiovascular pathology might result in severe hemodynamic/pulmonary/neurologic compromise (Prevention)

## Slide 54
THANK YOU VERY MUCH!